Folding Door Restrictor

|  | Folding Door Restrictor | Field Survey |
| --- | --- | --- |

F

NOTE: Use one survey sheet per car, unless all dimensions and landing configurations are the same.

1-2

2-3

3-4

4-5

5-6

6-7

7-8

8-9

9-10

10-11

11-12

12-13

13-14

14-15

15-16

16-17

17-18

18-19

19-20

| 1 |  |
| --- | --- |
| 2 |  |
| 3 |  |
| 4 |  |
| 5 |  |
| 6 |  |
| 7 |  |
| 8 |  |
| 9 |  |
| 10 |  |
| 11 |  |
| 12 |  |
| 13 |  |
| 14 |  |
| 15 |  |
| 16 |  |
| 17 |  |
| 18 |  |
| 19 |  |
| 20 |  |

NOTES:

- The table should have one more measurement for Entrance Heights than there are Hoistway Floor Heights.

- Above 20 floors, contact Unitec® for restrictor options. If job has rear entrances, contact Unitec® directly.

Fill Out:

Opening Type:

Center-Opening

Single-Slide

Two-Speed

Number of Cars:                                             Number of Landings per Car:

Quantity of Front Entrances:                           Quantity of Rear Entrances:

If you have Otis type 6940 door locks, provide length of car vane (cam) on the car door:

FOLDING DOOR RESTRICTOR

SPEC SHEET

February 2013

BENEFITS

- Maintenance-Free Passive Device

- No Moving Parts During Normal Elevator Operation

- Meets all requirements of ANSI A17.1 Rule 2.12.5 & Appendix B

- Low Cost

- For Center-Opening, Single-Slide, and 2-Speed Doors with 84 in. and 96 in. Entrance Heights

RUNNING & DOOR CLEARANCES

- 5.25 in. (+/- 0.125 in.) between car doors & hoistway doors with standard 1.25 in. running clearance sill-to-sill.

- Car door-to-hoistway sill nose must be greater than 2.75 in.

- Hoistway door-to-car sill nose must be greater than 3.375 in.

- Car door-to-hoistway door 5.25–5.50 in. permissible, but requires shims under angles.

CAR DOOR SPACE REQUIRED

84-in. Entrance Heights:

6.25 in. wide by 65.75 in. from trailing edge bottom of driven car door panel. Ensure no operator linkage passes through this space.

>84-in.–96-in. Entrance Heights: 6.25 in. wide by 77.75 in. from trailing edge bottom of driven car door panel. Ensure no operator linkage passes through this space.

NOTE: If these spaces are not available, you may still be able to use the Folding Door Restrictor, but the costs may increase. Call Unitec with the space you have available for more information.

FLOOR HEIGHT RESTRICTIONS

84-in. Entrance Heights:

Allowable sill-to-sill floor height range is 99 in. to 130.5 in.

96-in. Entrance Heights:

Allowable sill-to-sill floor height range is 111 in. to 154.5 in.

NOTE: If entrances heights fall outside these parameters or are not consistent within 1 in., contact Unitec for feasibility study and per-contract specification—additional costs apply.

# Text boxes

Hoistway Floor

Height (FH)

Entrance Height (EH)

Floor

Number

UNITEC PARTS COMPANY | Phone: 1 800 328 7840 | Fax: 1 860 286 1625 |   www.unitecparts.com

UNITEC PARTS COMPANY | Phone: 1 800 328 7840 | Fax: 1 860 286 1625 |   www.unitecparts.com

UNITEC PARTS COMPANY | Phone: 1 800 328 7840 | Fax: 1 860 286 1625 |   www.unitecparts.com

Email Survey to info@unitecparts.com or fax back to: (860) 286-1625